## Slide 1: EMCCD Speckle Interferometry at the US Naval Observatory
Rachel Matson (USNO)

## Slide 2: Speckle Interferometry
Speckle pattern due to phase fluctuations in the wavefront caused by seeing
Binary stars = superposition of two identical speckle patterns
Notes: - Speckle pattern due to seeing induced phase fluctuations on the wavefront
Auto-correlation function calculated from the power spectrum (calculated by summing the square modulus of the FT)

## Slide 3: Speckle Interferometry
Speckle pattern due to phase fluctuations in the wavefront caused by seeing
Binary stars = superposition of two identical speckle patterns
STF 1988: sep = 1.7”, 𝜃 = 250°
VA = 7.59, VB = 7.84
Notes: - Speckle pattern due to seeing induced phase fluctuations on the wavefront
Auto-correlation function calculated from the power spectrum (calculated by summing the square modulus of the FT)

## Slide 4: Speckle Interferometry
STF 1988: sep = 1.7”, 𝜃 = 250°
VA = 7.59, VB = 7.84
Notes: - Speckle pattern due to seeing induced phase fluctuations on the wavefront
Auto-correlation function calculated from the power spectrum (calculated by summing the square modulus of the FT)
Fringe spacing = binary separation, orientation = binary position angles, depth = magnitude difference

## Slide 5: Speckle Interferometry at GSU
“Encouraged by the success of the program of binary star speckle interferometry initiated at Georgia State in 1977, CHARA was established in 1984 with the goal of promoting, designing, funding and operating a major new instrument capable of achieving new levels of angular resolution.”
McAlister 1983
κ Uma
P = 36y
ρ = 0.3’’
Notes: Kappa Uma: sep = 0.3”, V ~ 4, obs since 1907
K UMa speckle photograph from McAlister 1983, PS from 50 speckle frames
- ~35 measures from McAlister/GSU speckle

## Slide 6: US Naval Observatory
Precise positions and magnitudes of celestial objects for navigation
‘Great equatorial’ 26-inch refractor built in 1873
Washington Double Star Catalog:
  > 2 million measures of 154,000 double stars
  ~3300 Visual Orbits
Notes: Observed solar system bodies and double stars
Masses of outer planets important for correct ephemerides

## Slide 7: Double Stars at USNO
Double star observing at USNO since 1890’s using micrometry and photographic techniques
In 1964 USNO took over Double Star Database
Speckle interferometry program began in 1990 using Intensified CCDs (ICCD)
Upgrade speckle camera to EMCCD in 2020
26-inch refractor
Notes: - Precise positions and magnitudes of celestial objects for navigation
- Observed solar system bodies and double stars
- WDS = successor to Index Catalogue of Visual Double Stars (1963). Three earlier double star catalogs in this century (1906, 1927, 1932) each covered portions of the sky
ICCD: 1990 – 2019
EMCCD: 6/2020

## Slide 8: Double Stars at USNO
USNO 26”
CHARA
SOAR
Gemini
0.01” 0.1” 1” 10” 100” 1000”
Delta Magnitude
Separation (arcsec)
Notes: “Accurate and precise measurement of bright, modest separation double stars neglected by programs on larger telescopes”
Gaia DR2: >1”, dm ~ 7
NPOI: 10 – 200 mas
USNO 26”: 0.2 – 60”
SOAR (4.1m = 13.5ft): 0.03 – 3”
Gemini (8m = 26.ft): 0.02 – 2”

## Slide 9: EMCCD Speckle Camera
Design, install, & calibration

## Slide 10: Camera Head Design
L1 (mm) | Pixel Scale (arcsec) | Field Size (arcsec)
20.0 | 0.090 | 92
40.0 | 0.180 | 184
Andor iXon 888 EMCCD
SBIG Filter Wheel
26” (0.66m) Refractor: F = 9.9m, F/D = 15
Notes: 26”: Refractor, lens diameter D = 0.66m focal length F = 9.9m, F/D = 15. The scale is 48 μm per arcsecond.
EMCCD: 13x13 μm, format 1024x1024 pixels (13x13mm).
Use achromatic doublet lenses for re-imaging the telescope focal plane onto the detector with different magnifications.
L1 collimates beam, L2 focuses on detector

## Slide 11: EMCCD + Camera Head Mounted
Notes: EMCCD delivered – 7/29/19
Camera head design – 2/18/20
Camera head printed – 4/16/20
EMCCD mounted – 5/8/20
Pointing + finder verification – 5/12/20
Focus adjustment – 6/3/20
First data recorded – 6/7/20

## Slide 12: Slit-Mask Calibration
Slit-spacing = 76.83mm
Wavelength = 55025nm
Mean scale (a) = 0.070030.00003”/pixel
Mean rotation (b) = 1.4200.096
HI/LOW scale = 4.4660.018
Notes: Calibration is performed with a slit-mask, precisely machined in the Instrument Shop, attached to lens end of the telescope.
  Slit-spacing = 76.83 mm
  Wavelength of observation = 55025 nm
  Multiple orientations done to determine aspect ratio of CCD.
Calibration is performed with a slit-mask, precisely machined in the Instrument Shop, attached to lens end of the telescope.
  Slit-spacing = 76.83 mm
  Wavelength of observation = 550±25 nm
  Multiple orientations done to determine aspect ratio of CCD.

## Slide 13: Separation (r) vs. Delta-m (Dm)

## Slide 14: ICCD vs. EMCCD Capabilities
Number of systems accessible: ICCD ∼ 42,000 vs. EMCCD ∼ 62,000
Notes: Fraction of doubles resolved below the line

## Slide 15: Double Star Observations
Notes: Jan – Nov 2021

## Slide 16: 2020 – 2022A Observations
Notes: 124 nights
7250 Observations
4103 Double star measures

## Slide 17: 2020 – 2022A Observations
Notes: 6024 Observations
3380 Double star measures
2891 good dm

## Slide 18: 2020 – 2022A Observations
0.2”
Min sep = 0.16”
Max sep = 87.63”
Mean sep = 7.37”
Median sep = 2.82”
Notes: 6024 Observations
3380 Double star measures
2891 good dm

## Slide 19: 2020 – 2022A Observations

## Slide 20: Speckle Delta Magnitudes
Speckle (PS)
Photometry (avg image)

## Slide 21: Speckle Delta Magnitudes
Notes: Avg 1+ resid: mean = 0.5, RMS = 0.90
Avg 3+ resid: mean = 0.23, rms = 0.48

## Slide 23: Summary
EMCCD Speckle camera installed at USNO
More than 4000 double stars observed from 2020 – 2022A
Characterizing uncertainties in r, 𝜃, Dm
Publish results & upload to WDS
https://crf.usno.navy.mil/wds

## Slide 25: Slit-Mask Calibration
Pixel aspect ratio 1:1
Mean scale (a) = 0.070030.00003”/pixel
Mean rotation (b) = 1.4200.096
HI/LOW scale = 4.4660.018
Chart: Scale in arcseconds per pixel
| 80 F | 65 F | 39 F | 28 F
Column1 | 0.070032 | 0.069999 | 0.070077 | 0.070021
Column2 | 0.071643 | 0.070909 | 0.070776 | 0.07028
Column3 | 0.068422 | 0.069089 | 0.069378 | 0.069762
Column4 | 0.070032 | 0.069999 | 0.070077 | 0.070021
Jun ‘21
Sep ‘20
Jan
‘21
Feb
‘21
Notes: Errors larger with higher temperatures, but this also corresponds to the brightest single star. This may be a temperature effect or may be a magnitude effect. However, what is significant is that the mean is unchanged : no change in scale with temperature.
50-60 HI/LO pairs

## Slide 26: Magnitude Limits
Name | Mag 1 | Mag 2 | Last | Sep | PA | Obs | Sep | PA | dm
STI2346 | 12.3 | 12.3 | 2017 | 15.5 | 105 | 2021.4799 | 15.59 | 103.9 | 0.6
HJ 1265 | 12.7 | 12.8 | 2015 | 9.9 | 271 | 2021.4798 | 9.91 | 270.5 | 0.9
KPP1502 | 13 | 13 | 2015 | 11.3 | 217 |  |  |  | 
HJ 262 | 13.3 | 13.1 | 2015 | 20.4 | 124 | 2021.48 | 20.44 | 123.8 | 0.5
POU3276 | 13.3 | 13.3 | 2015 | 6.4 | 120 | 2021.48 | 6.6 | 120.2 | 3.8
POU3279 | 13.7 | 13.7 | 2017 | 13.4 | 169 | 2021.48 | 13.59 | 168.9 | 1
KZA 113 | 13.7 | 14.1 | 2015 | 21 | 157 |  |  |  | 
KZA 116 | 13.8 | 13.8 | 2015 | 13.3 | 293 |  |  |  | 
LDS 991 | 14.1 | 14.2 | 2016 | 13 | 139 |  |  |  | 
DAM 948AC | 14.8 | 15.1 | 2015 | 9.9 | 278 |  |  |  | 
UC 2898 | 16.2 | 16.5 | 2015 | 6.7 | 330 |  |  |  | 

## Slide 27: Separation (r) vs. Delta-m (Dm)
= 309
Notes: Total = 309 doubles observed ~ Feb – Apr 2021

## Slide 28: 2020 – 2022A Observations
2020 Data:
Mean sep = 7.07
Median sep = 3.33
Mean dm = 1.90
Median dm = 1.4
Mean resolution limit = 0.21
Median resolution limit = 0.19
2021 Data:
Mean sep = 7.18
Median sep = 2.81
Mean dm = 1.96
Median dm = 1.5
Mean resolution limit = 0.24
Median resolution limit = 0.20
2022 Data:
Mean sep = 8.11
Median sep = 2.28
Mean dm = 2.10
Median dm = 1.8
Mean resolution limit = 0.25
Median resolution limit = 0.22

## Slide 29: 2020 – 2022A Observations

## Slide 30: Speckle delta magnitudes